## Slide 1: Designing Custom Circuit Boards
Michael Johnson-Moore
Presented Feb. 20, 2025 at StudentSPEAK
Elliot T. Bowers Honors College
Sam Houston State University
Notes: Everything in this presentation is simplified for laypeople.

## Slide 2: Thanks And Acknowledgements
Elliot T. Bowers Honors College
  Funding
  Hosting this presentation
Dr. Iftekhar Basith
  Faculty Advisor
Dean Bell
  Allowing me to do a thesis on this project.

## Slide 3: Thanks And Acknowledgements
American Society for Engineering Education
  Peer Review and Future Presentation (hopefully)
  Montreal, Canada, June 22-25, 2025
  Paper already accepted
Pabasar S.
  Artist of Title Font “Cirquee”

## Slide 4: Full Project Overview
2:01

## Slide 5: Full Project Overview
Research
Project
This
Presentation

## Slide 6: Full Project Overview
Modular Robotic Arm
Robotics experience
AI Experience
Future Prosthetics?

## Slide 7: Full Project Overview
Modular Robotic Arm
  Rigid Limb Segments

## Slide 8: Full Project Overview
Modular Robotic Arm
  Rigid Limb Segments

## Slide 9: Full Project Overview
Modular Robotic Arm
  Rigid Limb Segments

## Slide 10: Full Project Overview
Modular Robotic Arm
  Rigid Limb Segments

## Slide 11: Full Project Overview
Modular Robotic Arm
  Rigid Limb Segments

## Slide 12: Full Project Overview
Modular Robotic Arm
  Rigid Limb Segments

## Slide 13: Full Project Overview
Modular Robotic Arm
  Rigid Limb Segments

## Slide 14: Full Project Overview
Modular Robotic Arm
  Rigid Limb Segments
  Movable Joint Segments

## Slide 15: Full Project Overview
Modular Robotic Arm
  Rigid Limb Segments
  Movable Joint Segments

## Slide 16: Full Project Overview
Modular Robotic Arm
  Rigid Limb Segments
  Movable Joint Segments

## Slide 17: Full Project Overview
Modular Robotic Arm
  Rigid Limb Segments
  Movable Joint Segments

## Slide 18: Full Project Overview
Modular Robotic Arm
  Rigid Limb Segments
  Movable Joint Segments

## Slide 19: Full Project Overview
Modular Robotic Arm
  Rigid Limb Segments
  Movable Joint Segments
I don’t know how to animate
both limbs moving at once.

## Slide 20: Full Project Overview
Modular Robotic Arm
  Rigid Limb Segments
  Movable Joint Segments
I don’t know how to animate
both limbs moving at once.

## Slide 21: Full Project Overview
Modular Robotic Arm
  Rigid Limb Segments
  Movable Joint Segments
I don’t know how to animate
both limbs moving at once.

## Slide 22: Full Project Overview
Modular Robotic Arm
  Rigid Limb Segments
  Movable Joint Segments
I don’t know how to animate
both limbs moving at once.

## Slide 23: Full Project Overview
Modular Robotic Arm
  Rigid Limb Segments
  Movable Joint Segments
I don’t know how to animate
both limbs moving at once.

## Slide 24: Full Project Overview
Modular Robotic Arm
  Rigid Limb Segments
  Movable Joint Segments
I don’t know how to animate
both limbs moving at once.

## Slide 25: Full Project Overview
Modular Robotic Arm
  Rigid Limb Segments
  Movable Joint Segments
I don’t know how to animate
both limbs moving at once.

## Slide 26: Full Project Overview
Modular Robotic Arm
  Rigid Limb Segments
  Movable Joint Segments
  Central Controller

## Slide 27: Full Project Overview
Modular Robotic Arm
  Rigid Limb Segments
  Movable Joint Segments
  Central Controller
Proximal
Distal

## Slide 28: Ideal – Any Shape you Need

## Slide 29: Sensors – collision avoidance

## Slide 30: Sensors – collision avoidance

## Slide 31: Sensors – collision avoidance

## Slide 32: Sensors – Two Types
Capacitive Touch Sensing
Inductive Proximity Sensing

## Slide 33: Sensors – Two Types
Capacitive Touch Sensing
Inductive Proximity Sensing

## Slide 34: Sensors – Two Types
Capacitive Touch Sensing
Short Range
Inductive Proximity Sensing
2-4 mm

## Slide 35: Sensors – Two Types
Capacitive Touch Sensing
Short Range
Inductive Proximity Sensing
2-4 mm
12.5 mm

## Slide 36: Sensors – Two Types
Capacitive Touch Sensing
Short Range
Inductive Proximity Sensing
Only Detects Metal
2-4 mm
12.5 mm

## Slide 37: Simplified Model

## Slide 38: Limb Segment
¼ inch
>

## Slide 41: Communications Method Options
Traditional networking – IP addressing & GOOSE/DNP3
Onion-tree routing
Input Modification Routing
Vector Input Modification
Machine Learning Neuron
Neuron-integrated neural network input modification
Biological neuron chemical neurotransmitter simulation
Traditional networking – IP addressing & GOOSE/DNP3
Onion-tree routing
Input Modification Routing
Vector Input Modification
Machine Learning Neuron
Neuron-integrated neural network input modification
Likely too high resource cost on RP2040s
Limited scalability
Error-prone
Complex arm programming
Limited scalability

## Slide 42: Goals after Production
Design and build joints, central controller
Program the CPUs
Communication and control experiments
Write Thesis
Present at URS
Present at ASEE Conference

## Slide 43: Overview of PCB Design
2:10

## Slide 44: Overview of PCB Design
PCB – Printed Circuit Board
Electronic circuit acid-etched onto copper
Multiple layers
Components – resistors, integrated circuits, etc.

## Slide 45: Multiple Layers
Components on outer layers
Signals/Power on inner layers
Solder Spots called “pads”
Wires called “traces”
“Vias” connect layers
Image Source: JLCPCB (https://jlcpcb.com/) Feb. 16, 2025

## Slide 46: Design Process
Select Major Components – CPUs, connectors, etc.
Place components on schematic, select “footprint”
Connect Pins
Send to PCB Design
This design is simplified and would not actually work.

## Slide 47: Design Process
Setup CAD Software
Define Board Edge
Place “footprints” where desired.

## Slide 48: Color meaning
Red – Copper on top layer
Blue – Copper on bottom layer
Gold – Copper on all layers
Pink and thick gray – component area
Thin gray – board outline (cuts)
Blue lines – pads should connect
Yellow – Printed on Board

## Slide 49: Design Process
Run traces between pads which need to connect.

## Slide 50
Modern CAD Software will not allow connecting the wrong pads

## Slide 51: Design Process
Power pins need thicker traces, however…

## Slide 52: Design Process
… It’s good practice to use fill zones

## Slide 54: Design Process
Use vias to connect copper between layers.

## Slide 55: Other considerations
Thermal spokes for easy soldering

## Slide 56: Other considerations
Length tuning
Minimize signal delay difference

## Slide 57: Other considerations
Signal delayed

## Slide 58: Other considerations
Bent track increases delay

## Slide 59: Other Considerations
Pullup/down resistors
Decoupling capacitors

## Slide 60: What are these?
Resistor
Capacitor
FREE
Cars!

## Slide 61: Original (Scrapped) Design
2:15

## Slide 62: Original Concept

## Slide 63: Original Concept
6 modules/in
Wrap around PVC
Right angle screw things

## Slide 64: Issues with original design
USB Port
Cost
  Right angle screw things!
  Inefficient IO usage – 1 sensor controller per module!
  $8500 for 5 feet!
Space

## Slide 65: Original Concept

## Slide 66: Current Design
2:18

## Slide 67: Current (Final?) Board

## Slide 68: Connectors and Mounting Holes
For Sensor Board
  Amphenol F31L-1A7H1-11070 and F31L-1A7H1-11015
  Many pins! Discontinued?

## Slide 69: Connectors and Mounting Holes
For Sensor Board
  Amphenol F31L-1A7H1-11070 and F31L-1A7H1-11015
  Many pins! Discontinued?

## Slide 70: Connectors
For segment connections
  Metz Connect FR202XXHBDN and PR202XXHBDN
  Compatible! Discontinued?

## Slide 71: Connectors
For segment connections
  Metz Connect FR202XXHBDN and PR202XXHBDN
  Compatible! Discontinued?

## Slide 72: RP2040 layout
Raspberry Pi RP2040
  Used in Pico
Cheap - $1.00 (≈$4.00 w/ requirements)
Fast enough – 133 MHz
  Much faster than Arduino Uno – 16 MHz
Large number of I/O pins

## Slide 73: RP2040 layout
Raspberry Pi RP2040
  Used in Pico
Cheap - $1.00 (≈$4.00 w/ requirements)
Fast enough – 133 MHz
  Much faster than Arduino Uno – 16 MHz
Large number of I/O pins

## Slide 74: Required By RP2040
NAND Flash (storage) – Winbond W25Q128JVS
  W25Q128JVSIQ variant for 4 data lines

## Slide 75: Required By RP2040
12 MHz Clock crystal – Abracon ABM8-272-T3

## Slide 76: Required By RP2040
3.3V Voltage regulator – Onsemi NCP1117

## Slide 77: Required By RP2040
1 μF low ESR capacitors
  Shipment delay
Various other resistors and capacitors

## Slide 78: LDC3114 Inductive Sensor Controllers
Texas Instruments LDC3114QPWRQ1
Automotive version
  NOT cheap, no minimum order
Not small
  LDC2114 is available small
Complicated
12.5 mm

## Slide 79: LDC3114 Inductive Sensor Controllers
Texas Instruments LDC3114QPWRQ1
Automotive version
  NOT cheap, no minimum order
Not small
  LDC2114 is available small
Complicated

## Slide 80: Current (Final?) Board

## Slide 81: Required by LDC3114
A low capacitance, low ESR, low ESL capacitor
  C0402C222J3GACAUTO
Various other resistors and capacitors

## Slide 82: Required by LDC3114
Copper fill
Specially designed spiral

## Slide 83: CAP1206 Capacitive sensor controllers
Microchip CAP1206-TR-AIA
Cheap, decent number of channels
Simple
Small
Requires various resistors and capacitors
2-4 mm

## Slide 84: CAP1206 Capacitive sensor controllers
Microchip CAP1206-TR-AIA
Cheap, decent number of channels
Simple
Small
Requires various resistors and capacitors

## Slide 85: USB HUB

## Slide 86: USB HUB Controller
Infineon CY7C65632-28LTXCT
Four downstream USB ports
  1 to each RP2040
  1 to next module
Cheap
Small

## Slide 87: Required by USB HUB
EEPROM (Storage) – limited, discontinued options
  Optional

## Slide 88: Required by USB HUB
EEPROM (Storage) – limited, discontinued options
  Optional

## Slide 89: Required by USB HUB
12 MHz Clock crystal – Abracon ABM8-272-T3
  Can’t share 

## Slide 90: Required by USB HUB
LED – optional?

## Slide 91: Required by USB HUB
649 Ω resistor – RT0402BRD07649RL
  Tolerance? – ±0.1%
Various other resistors and capacitors

## Slide 92: Current (Final?) Board

## Slide 93: Logic Gates
Texas Instruments SN74HCS30PWR and SN74HC32PWR
  Discrete logic gates (NAND and OR).

## Slide 94: Current (Final?) Board

## Slide 95: Sensing Board
Image Source: JLCPCB Engineers
I paid for this image to be produced.

## Slide 96: Sensing Board

## Slide 97: Sensing Board Up Close

## Slide 98: Issues Encountered
2:31

## Slide 99: EAR99
JLCPCB requires EAR99 if IC
EAR99 – US export regulation?
Repurchased some parts

## Slide 100: LDC2114 Size
Kicad footprint - 0.5 mm pitch
Actual component - 0.4 mm pitch
Not manufacturable

## Slide 101: Bad component choices
CAP1208? CAP1214?
esp32?
Discontinued stuff

## Slide 102: RP2040 GPIO USAGE
RP2040 supports 2 active I2C channels.
Workaround.
I2C multiplexer?
102

## Slide 103: Manufacturer Confusion
Engineers thought Test Points Desired
Don’t expect English
Don’t assume contractors read

## Slide 104: Component Delays

## Slide 105: Component Delays

## Slide 106: Assembly
Screws take up space
106

## Slide 109: Raspberry Pi RP235xX
RP2040
133 MHz
264 kB RAM
External storage
RP235xX
150 MHz (++performance)
520 kB RAM
[Optional] internal storage

## Slide 110: References
D. Hou and D. Dolezilek, “IEC 61850 – what it can and cannot offer to traditional protection schemes,” SEL Journal of Reliable Power, vol. 1, no. 2, Oct. 2010. [Online]. Available: https://cdn.selinc.com/assets/Literature/Publications/Technical%20Papers/6335_IEC61850_DH-DD_20080912_Web.pdf
R. Lent, F. A. C. Azevedo, C. H. Andrade-Moraes, and A. V. O. Pinto, “How many neurons do you have? some dogmas of quantitative neuroscience under revision,” European Journal of Neuroscience, vol. 35, no. 1, pp. 1–9, 2012. [Online]. Available: https://onlinelibrary.wiley.com/doi/abs/10.1111/j.1460-9568.2011.07923.x
M. Islam, G. Chen, and S. Jin, “An overview of neural network,” American Journal of Neural Networks and Applications, vol. 5, no. 1, pp. 7–11, 2019. [Online]. Available: https://doi.org/10.11648/j.ajnna.20190501.12
(2021, Aug.) Inductive sensing design calculator tool. Texas Instruments. [Online]. Available: https://www.ti.com/tool/download/ LDC-CALCULATOR-TOOLS
RP2040 Datasheet: A microcontroller by Raspberry Pi, eec2b0cclean ed., Raspberry Pi, Oct. 2024. [Online]. Available: https://datasheets.raspberrypi.com/rp2040/rp2040-datasheet.pdf
Raspberry Pi Pico Pinout, Raspberry Pi. [Online]. Available: https://datasheets.raspberrypi.com/pico/Pico-R3-A4-Pinout.pdf
Hardware design with RP2040: Using RP2040 microcontrollers to build boards and products, 2nd ed., Raspberry Pi, Oct. 2024. [Online]. Available: https://datasheets.raspberrypi.com/rp2040/hardware-design-with-rp2040.pdf
spiflash® 3V 128M-BIT SERIAL FLASH MEMORY WITH DUAL/QUAD SPI & QPI & DTR, C ed., winbond, Mar.2018. [Online]. Available: https://www.winbond.com/resource-files/w25q128jv_dtr%20revc%2003272018%20plus.pdf
1.0 A Low-Dropout Positive Fixed and Adjustable Voltage Regulators NCP1117, NCP1117I, NCV1117, 31st ed., onsemi, Aug. 2021. [Online]. Available: http://www.onsemi.com/pub_link/Collateral/NCP1117-D.PDF
CAP1206: 6-Channel Capacitive Touch Sensor, DS00001567B ed., Microchip Technology, Nov. 2015. [Online]. Available: https://www.microchip.com/en-us/product/cap1206
LDC3114 4-Channel Hybrid Inductive Touch and Inductance to Digital Converter, 1st ed., Texas Instruments, Dec. 2021. [Online]. Available: https://www.ti.com/lit/ds/symlink/ldc3114.pdf
LDC2112, LDC2114 Inductive Touch Solution for Low-Power HMI Button Applications, B ed., Texas Instruments, Jan. 2017. [Online]. Available: https://www.ti.com/lit/ds/symlink/ldc2114.pdf
SN5430, SN54LS30, SN54S30, SN7430, SN74LS30, SN74S30, 8-Input Positive-NAND Gates, Texas Instruments, Mar. 1988. [Online]. Available: https://www.ti.com/lit/ds/symlink/sn74ls30.pdf
SN5432, SN54LS32, SN54S32, SN7432, SN74LS32, SN74S32, Quadruple 2-Input Positive-OR Gates, Texas Instruments, Mar. 1988. [Online]. Available: https://www.ti.com/lit/ds/symlink/sn74ls32.pdf
CY7C65632, CY7C65634: HX2VL - Very Low-Power USB 2.0 Hub Controller, O ed., infineon, Oct. 2024. [Online]. Available: https://www.infineon.com/dgdl/Infineon-CY7C65632_CY7C65634_HX2VL_VERY_LOW-POWER_USB_2.0_HUB_CONTROLLER-DataSheet-v14_00-EN.pdf?fileId=8ac78c8c7d0d8da4017d0ecd35994769&utm_source=cypress&utm_medium=referral&utm_campaign=202110_globe_en_all_integration-files&redirId=File_1_1_521
Data sheet: FR202xxHBDN, W ed., Metz Connect, Dec. 2024. [Online]. Available: https://media.metz-connect.com/files/171/Data_sheet_FR202XXHBDN.PDF
Data sheet: PR202xxHBDN, W ed., Metz Connect, Dec. 2024. [Online]. Available: https://media.metz-connect.com/files/171/Data_sheet_PR202XXHBDN.PDF
2:41

## Slide 111: Questions?